## Shopping List
Amount	Part Type	Properties
8	Ceramic Capacitor	capacitance 100nF; package 200 mil [THT, multilayer]; voltage 16V
1	Electrolytic Capacitor	capacitance 100µF; package 100 mil [THT, electrolytic]; voltage 10V
1	DOIT Esp32 DevKit v1	variant 1; pins 30; part number ESP32S-PIN30
1	Basic FET P-Channel	type p-channel; package TO220 [THT]
1	Generic male header - / 4 pins	hole size 1.0mm,0.508mm; row single; package THT; form ♂ (male); pins 4; pin spacing 0.1in (2.54mm)
8	PCF8574	variant variant 1; type PCF8574; package DIP16 [THT]
16	Generic male header - / 8 pins	hole size 1.0mm,0.508mm; row single; package THT; form ♂ (male); pins 8; pin spacing 0.1in (2.54mm)
2	Red (633nm) LED	leg yes; current 0.030; color Red (633nm); package 5 mm [THT]
32	Pad	layer copper0
32	Pad	layer copper1
1	Generic male header - / 2 pins	hole size 1.0mm,0.508mm; row single; package THT; form ♂ (male); pins 2; pin spacing 0.1in (2.54mm)
66	330Ω Resistor	resistance 330Ω; tolerance ±5%; bands 4; power 0.25; package THT; pin spacing 400 mil
64	100Ω Resistor	resistance 100Ω; tolerance ±5%; bands 4; power 0.25; package THT; pin spacing 400 mil
1	Generic male header - / 3 pins	hole size 1.0mm,0.508mm; row single; package THT; form ♂ (male); pins 3; pin spacing 0.1in (2.54mm)
16	Sharp PC847X	part PC847X; package THT